## Slide 1
Introduction to Circuits Analysis
by Andrew G. Bell
abell118@ivytech.edu
(260) 481-2288
Lecture 4

## Slide 2: CHAPTER 4
Series Circuits

## Slide 3: Series Circuits
Definition: One path for current flow
Key Characteristic: The current is the same at any point in the circuit.

## Slide 4: Series Circuits (cont.)
Total resistance in a series circuit is the summation of the individual resistor values:
RT = R1 + R2 + R3 … + Rn
Where n = the number of resistors

## Slide 5: Series Circuits (cont.)
Total resistance in a series circuit can also be found using Ohm’s law.
Total resistance is equal to the circuit voltage divided by the current flowing in the circuit.

## Slide 6: Mathematical Expression
Remember, IT is the same at any point in the circuit.

## Slide 7: Ohm’s Law
The equation may also be arranged to solve for Total Voltage (VT) or Total Current (IT):

## Slide 8: Concept of Voltage Drop
A voltage drop is typically thought of as a voltage produced by allowing a current to flow through a resistance.

## Slide 9: Voltage Drops in a Series Circuit
The voltage drop across a resistor in a series circuit is produced from the current flow through the resistor.

## Slide 10: Calculating a Voltage Drop
If there are two resistors in a series circuit, each voltage drop may be calculated by using the following equations:
VR1 = IT x R1
VR2 = IT x R2

## Slide 11: Voltage Divider Rule
The voltage across any resistor in a series may be determined by using the following equation:

## Slide 12: Term Definitions
VX: Voltage across the desired resistor
RX: Value of the desired resistor
VT: The circuit applied voltage

## Slide 13: Kirchhoff’s Voltage Law
An important concept used in simple to very complex circuits
It allows one to solve problems and check answers
Used with Ohm’s law to solve difficult problems

## Slide 14: Kirchhoff’s Voltage Law (cont.)
Kirchhoff’s Voltage Law (KVL) states:
The arithmetic summation of all voltage drops in a series circuit will always equal the applied voltage
and/or
The algebraic summation of the voltages around a loop will always equal zero volts

## Slide 15: Kirchhoff’s Voltage Law (cont.)

## Slide 16: Power in Series Circuits
Remember the basic equations:

## Slide 17: Power in Series Circuits (cont.)
Because current is the same at every point in a series circuit, the resistance with the smallest value will also dissipate the smallest power value.
The largest resistor in the circuit will dissipate the largest amount of power.

## Slide 18: Power in Series Circuits (cont.)
Since the current is the same at any point in a series circuit, the equation
P = I2 x R is perhaps the best equation to use when I and R are known.
Thus, PR1 = I2 x R1 and PR2 = I2 x R2, etc.

## Slide 19: Power in Series Circuits (cont.)
The total power dissipated in a series circuit is also the amount of power the power source must deliver. This may also be expressed as:
PT = PR1 + PR2 … + PRn

## Slide 20: Power in Series Circuits (cont.)
The total power may also be calculated using Watt’s law:
PT = I2 x RT

## Slide 21: Opens in a Series Circuit
An open circuit occurs anytime a break in the current path occurs.
If an open occurs at any point, current will decrease to 0 A.
All voltage drops will decrease to 0 V.

## Slide 22: Opens in a Series Circuit (cont.)
An interesting aspect of an open is that the applied voltage will appear across the open point in the circuit.

## Slide 23: Shorts in a Series Circuit
A short is an undesired, very low resistance path in or around a given circuit.
If a short occurs, current will increase because resistance decreases.
As current increases, the voltage across the remaining resistors will increase.

## Slide 24: Shorts in a Series Circuit (cont.)
If a total short occurs, RT = 0 .
Current will attempt to increase to unacceptable levels.

## Slide 25: Shorts

## Slide 26: Multiple Voltage Sources in Series
Series Aiding:
  Negative terminal of one source is connected to the positive terminal of the other
Individual voltage sources add directly together:
VT = V1 + V2

## Slide 27: Multiple Voltage Sources in Series (cont.)
Series Opposing:
  Negative terminal of one source is connected directly to the negative terminal of the second
Voltage sources subtract and result is polarized in direction of the greater source:
VT = V1 – V2

## Slide 28: Voltage Divider
Resistive circuits used to obtain some percentage of the applied voltage source

## Slide 29: Voltage Reference Points
The concept of voltage has both magnitude and polarity.
Specific points in a circuit to measure voltage
  e.g., Vab or Vb

## Slide 30: Voltage Reference Points (cont.)
The voltage measured at the first subscript notation is with respect to the second subscript.
  e.g., Vab = -Vba

## Slide 31: Voltage Reference Points (cont.)

## Slide 32: Simpler Troubleshooting
Symptoms: Gather, verify and analyze
Identify: Possible areas of trouble
Make: Decisions—what, where
Perform: Tests or measurements
Locate: Narrow problem area
Examine: New location
Repeat: Procedure until problem found

## Slide 33: Troubleshooting Levels
Block or module
Component
System