## Slide 1
LAB
NOTEBOOK
EECT 101-50C
MR. TOTH
SPRING 2015
BY:
ALCIDES SEGOVIA

## Slide 2: Labs
Lab 1 – Test Equipment Intro and Resistors 3
Lab 2 – Resistors, DMM and Ohm’s Law 7
Lab 3 – Resistors, Multisim and Ohm’s Law 12
Lab 4 – Test Equipment Basics 15
Lab 5 – Test Equipment, Capacitors, and Inductors 22
Lab 6 – Learn to Solder 25
Lab 7 – CD-1 Checkout and 1st Solder Kit 28
Lab 8 – 555 Timer Chip 34
Lab 9 – Filters 38
Lab 10 – Square Wave to Sine Wave 42
Lab 11 – Troubleshoot Home Electronics 45
Lab 12 – Lissajous Pattern 52
Lab 13 – AC to DC Power Supplies 54
Lab 14 – ESD 57
Lab 15 – Test Old 0-30VC 61
Lab 16 – Soldering 63

## Slide 3: Lab 1 - Test Equipment Intro and Resistors
Objective
  Learn the test equipment.
    Digital Multimeter (DMM)
    Function Generator
    Oscilloscope (a.k.a. scope)
    Power Supply (fixed and programmable)
    LCR Meter
Research and Information on Test Equipment
  Watched videos on test equipment and how to use them. https://online.ivytech.edu/bbcswebdav/pid-24889078-dt-content-rid-58475683_1/courses/EECT101-50C-C1-201430/EECT101-50C-C1-201430_ImportedContent_20150114121945/ee101_vids_inst.htm
Test Equipment

## Slide 4: Testing Resistors
Objective
  Learn what a resistor is.
  Learn the resistor color code.
  Learn Ohm’s law.
  Measure 3 resistors.
Equipment and Material
  DMM
  Resistors: 1kΩ, 300Ω, and 39kΩ
Research and Information
  Watched videos on how to use DMM to measure resistors. (https://online.ivytech.edu/bbcswebdav/pid-24889078-dt-content-rid-58475683_1/xid-58475683_1)
  Watched video on resistor color codes. (https://online.ivytech.edu/bbcswebdav/pid-24974867-dt-content-rid-58475684_1/xid-58475684_1)
Lab 1 - Test Equipment Intro and Resistors

## Slide 5: Measuring Resistors
Lab 1 - Test Equipment Intro and Resistors
 | 1st digit | 2nd digit | 3rd digit | Tolerance | Resistance according to color |  |  |  |  | 
1 | br | bl | r | gd | R |  | Range |  |  | DM Reading
 | 1 | 0 | 100 | 0.05 | 1000 | Ohms | 950 | to | 1050 | 999
2 | o | o | br | gd | R |  | Range |  |  | DM Reading
 | 3 | 3 | 10 | 0.05 | 330 | Ohms | 313.5 | to | 346.5 | 324.16
3 | o | w | o | gd | R |  | Range |  |  | DM Reading
 | 3 | 9 | 1000 | 0.05 | 39000 | Ohms | 37050 | to | 40950 | 38731

## Slide 6
Lab 1 - Test Equipment Intro and Resistors
Summary and Conclusion
Summary
  We were introduced to the test equipment.
  We learned what a resistor is.
  We learned about the resistor color code. (BBROYGBPGWGS)
  We learned Ohm’s law.
  We measure 3 resistors.
Conclusion
  The resistors that were measured fell between the tolerance of each resistor.

## Slide 7: Lab 2 - Resistors, DMM and Ohm’s Law
Objective
  Learn how to use a Multimeter to measure resistance.
  Measure 5 different resistors
  Calculate expected value of 5 resistors in series and in parallel.
  Put resistors in series and then in parallel.
  Measure the currents.
  Compare calculated with measured
Equipment and Material
  Multimeter
  Resistors: 330Ω, 820Ω, 2.2kΩ, 4.7 k Ω, and 1.0 kΩ
Research and Information
  Review Ohm’s law power point

## Slide 8: Lab 2 - Resistors, DMM and Ohm’s Law
Measurements
R (Series) | Calculated | Measured | Max | Min | 
R1 | 330.00 | 325.13 | 346.50 | 313.50 | Ohms
R2 | 820.00 | 818.1 | 861.00 | 779.00 | Ohms
R3 | 2.2E+3 | 2162.2 | 2.3E+3 | 2.09E+3 | Ohms
R4 | 4.7E+3 | 4598.8 | 4.9E+3 | 4.465E+3 | Ohms
R5 | 1.0E+3 | 978.4 | 1.1E+3 | 950.00 | Ohms
R1-3 | 3.35E+3 | 3.31E+3 | 3.52E+3 | 3.18E+3 | Ohms
R1-5 | 9.05E+3 | 8.88E+3 | 9.50E+3 | 8.60E+3 | Ohms
IT (1-3) | 1.5E-3 | 1.45E-3 | 1.5E-3 | 1.40E-3 | mA
IT (1-5) | 545.6E-6 | 499.13E-6 | 572.9E-6 | 518.4E-6 | µA
V | 4.938 |  |  |  | 
R (Parallel) | Calculated | Measured | Max | Min | 
R1 | 330.00 | 325.13 | 346.50 | 313.50 | Ohms
R2 | 820.00 | 818.1 | 861.00 | 779.00 | Ohms
R3 | 2.2E+3 | 2162.2 | 2.3E+3 | 2.1E+3 | Ohms
R4 | 4.7E+3 | 4598.8 | 4.9E+3 | 4.5E+3 | Ohms
R5 | 1.0E+3 | 978.4 | 1.1E+3 | 950.00 | Ohms
R1-3 | 212.57 | 210.16 | 223.20 | 201.94 | Ohms
R1-4 | 203.37 | 200.93 | 213.54 | 193.20 | Ohms
IT (1-3) | 23.2E-3 | 22.31E-3 | 24.4E-3 | 22.1E-3 | mA
IT (1-4) | 24.3E-3 | 23.29E-3 | 25.5E-3 | 23.07E-3 | mA
V | 4.938 |  |  |  | 

## Slide 9: In Series

## Slide 10
In Parallel

## Slide 11: Lab 2 - Resistors, DMM and Ohm’s Law
Summary and Conclusion
Summary
  We learned how to use a Multimeter to measure the resistance of a resistor.
  We measured 5 different resistors individually.
  We calculate the expected value of the 5 resistors in series, and then in parallel.
  We put the 5 resistors in series and then in parallel.
  We measure the currents in both.
  Compared the calculated value with measured value.
Conclusion
  Current can be calculated.
  Measured values were with-in the tolorence.

## Slide 12: Lab 3 - Resistors, Multisim and Ohm’s Law
Objective
  Use Multisim to create 5 resistors in series and parallel.
  Use Multimeter to measure resistance.
  Compare calculated in multisim with measured
Equipment and Material
  Multimeter
  Multisim
  Resistors: 330Ω, 820Ω, 2.2kΩ, 4.7 k Ω, and 1.0 kΩ
Research and Information
  Review Ohm’s law power point
  Watch Multisim videos in blackboard

## Slide 13: Lab 3 - Resistors, Multisim and Ohm’s Law
Different Resistor Set-ups

## Slide 14: Multisim vs Measured
Lab 3 - Resistors, Multisim and Ohm’s Law

## Slide 15: Lab 3 - Resistors, Multisim and Ohm’s Law
Summary and Conclusion
Summary
  Learned Ohm’s Law
  Resistors were tested to see if the were within tolerance.
Conclusion
  Current can be calculated.
  Measured values were with-in the tolorence.

## Slide 16: Lab 4 Test Equipment Basics
Objective
  Use the Function Generator to provide different measurements.
  Use Oscilloscope to verify the output.
Equipment and Material
  Function Generator
  Oscilloscope
  DMM
Research and Information
  Watched videos on how to use the Function Generator and Ocilloscope in https://online.ivytech.edu/bbcswebdav/pid-24889087-dt-content-rid-58475674_1/courses/EECT101-50C-C1-201430/EECT101-50C-C1-201430_ImportedContent_20150114121945/ee101_vids_oscilloscope.htm

## Slide 17: Lab 4 Test Equipment Basics
1st Set-up
1.a. | Set up the Function Generator to provide a 100Hz sine wave at 1V P-P. |  |  |  |  |  |  | 
 | Record the settings of the Function Generator. |  |  |  |  |  |  | 
 | Frequency button = 100, Sine wave pushed |  |  |  |  |  |  | 
 | Nobs pushed in: DUTY, CMOS, OFFSET |  |  |  |  |  |  | 
 | Pulled out: Ampl to about the 11'o clock mark |  |  |  |  |  |  | 
1.b. | Use an Oscilloscope to verify the output of the function generator. Record the settings of the |  |  |  |  |  |  | 
 | Oscilloscope. |  | (Horiz scale X # of divisions = period. Vert scale X # of div = amplitude) |  |  |  |  | 
 | Period (Horizontal): 4 divisions x 2.5 ms = 10ms |  |  |  |  |  |  | 
 | Amplitude (Vertical): 1 division x 1 volt = 1V |  |  |  |  |  |  | 
1.c. | Measure the following: |  |  |  |  |  |  | Units:
 | a. | Period of the sine wave |  |  |  | 10 |  | ms
 | b. | Amplitude of the sine wave |  |  |  | 1 |  | Vrms
 | c. | Rise time of the sine wave |  |  |  | 5 |  | ms
 | d. | Fall time of the sine wave |  |  |  | 5 |  | ms

## Slide 18: Lab 4 Test Equipment Basics
2nd Set-up
2.a. | Set up the Function Generator to provide a 1KHz square wave at 5V P-P, 50% duty cycle. |  |  |  |  |  |  | 
 | Record the settings of the Function Generator. |  |  |  |  |  |  | 
 | Frequency button = 1k, square wave pushed |  |  |  |  |  |  | 
 | Nobs pushed in: DUTY, CMOS, OFFSET |  |  |  |  |  |  | 
 | Pulled out: Ampl to about the 9'o clock mark |  |  |  |  |  |  | 
2.b. | Use an Oscilloscope to verify the output of the function generator. Record the settings of the |  |  |  |  |  |  | 
 | Oscilloscope. |  | (Horiz scale X # of divisions = period. Vert scale X # of div = amplitude) |  |  |  |  | 
 | Period (Horizontal): 4 divisions x 250 µs = 1ms |  |  |  |  |  |  | 
 | Amplitude (Vertical): 1 division x 5 v = 5V |  |  |  |  |  |  | 
 | Pulse (Horizontal): period x 50% duty cycle |  |  |  |  |  |  | 
2.c. | Measure the following: |  |  |  |  |  |  | Units:
 | a. | Period of the square wave |  |  |  | 1 |  | ms
 | b. | Pulse width of the square wave |  |  |  | 500 |  | µs
 | c. | Amplitude of the square wave |  |  |  | 5 |  | V
 | d. | Rise time of the square wave |  |  |  | 250 |  | ns
 | e. | Fall time of the square wave |  |  |  | 250 |  | ns

## Slide 19: Lab 4 Test Equipment Basics
3rd Set-up
3.a. | Change the square wave to an 80/20 duty cycle. Record the settings of the Function Generator. |  |  |  |  |  |  | 
 | Frequency button = 1k, square wave pushed |  |  |  |  |  |  | 
 | Nobs pushed in: CMOS, OFFSET |  |  |  |  |  |  | 
 | Pulled out: Ampl to about the 9'o clock mark, DUTY to about the 4'o clock |  |  |  |  |  |  | 
3.b. | Use an Oscilloscope to verify the output of the function generator. Record the settings of the |  |  |  |  |  |  | 
 | Oscilloscope. |  | (Horiz scale X # of divisions = period. Vert scale X # of div = amplitude) |  |  |  |  | 
 | Period (Horizontal): 4 divisions x 250 µs = 1ms |  |  |  |  |  |  | 
 | Amplitude (Vertical): 2.5 division x 2 v = 5V |  |  |  |  |  |  | 
 | Pulse (Horizontal): period x 80/20 duty cycle |  |  |  |  |  |  | 
3.c. | Measure the following: |  |  |  |  |  |  | Units:
 | a. | Period of the square wave |  |  |  | 1 |  | ms
 | b. | Pulse width of the square wave |  |  |  | 0.8 |  | ms
 | c. | Amplitude of the square wave |  |  |  | 5 |  | V
 | d. | Rise time of the square wave |  |  |  | 250 |  | ns
 | e. | Fall time of the square wave |  |  |  | 250 |  | ns

## Slide 20: Lab 4 Test Equipment Basics
4th Set-up
4.a. | Change the square wave to a one-shot that is high for 10ms and off for the rest of the 1000ms period. |  |  |  |  |  |  | 
 | Record the settings of the Func Generator. |  |  |  |  |  |  | 
 | Frequency button = 100 Hz, Reading 9.95 Hz, square wave pushed |  |  |  |  |  |  | 
 | Nobs pushed in: CMOS, OFFSET |  |  |  |  |  |  | 
 | Pulled out: Ampl to about the 9'o clock mark, DUTY to about the 7'o clock |  |  |  |  |  |  | 
4.b. | Use an Oscilloscope to verify the output of the function generator. Record the settings of the |  |  |  |  |  |  | 
 | Oscilloscope. |  |  |  |  |  |  | 
 | Period (Horizontal): 1.4 divisions x 10.0 ms = 14ms ( Reached limitation on Function generator) |  |  |  |  |  |  | 
 | Amplitude (Vertical): 4.8 division x 1 v = 4.8V |  |  |  |  |  |  | 
 | Pulse (Horizontal): period x 80/20 duty cycle |  |  |  |  |  |  | 
4.c. | Measure the following: |  |  |  |  |  |  | Units:
 | a. | Period of the square wave |  |  |  | 14 |  | ms
 | b. | Pulse width of the square wave |  |  |  | 0.1 |  | ms
 | c. | Amplitude of the square wave |  |  |  | 4.8 |  | v
 | d. | Rise time of the square wave |  |  |  | 0.25 |  | ms
 | e. | Fall time of the square wave |  |  |  | 0.25 |  | ms

## Slide 21: Lab 4

## Slide 22: Lab 4 Test Equipment Basics
Summary and Conclusion
Summary
  Use the Function Generator to provide 4 different waves to measurements.
  Use Oscilloscope to verify the wave output.
Conclusion
  We were able to measure the waves
    Period
    Amplitude
    Rise/Fall

## Slide 23: Lab 5 - Test Equipment, Capacitors, and Inductors
Objective
  Use the LCR meter to measure inductors and capacitors. Including hand-wound inductors
  Measure: 4 Capacitors and 3 Standard Inductors
  Measure 3 hand-wound Inductors
Equipment and Material
  Capacitors: 4.7 pF, .0033 µF, .01 µF, and 4.7 µF
  LCR Meter, Oscilloscope, Function Generator
Research and Information
  Watched videos on Inductors: https://online.ivytech.edu/bbcswebdav/pid-24889093-dt-content-rid-58475677_1/courses/EECT101-50C-C1-201430/EECT101-50C-C1-201430_ImportedContent_20150114121945/ee101_vids_inductors.htm
  Watched videos on Capacitors: https://online.ivytech.edu/bbcswebdav/pid-24889094-dt-content-rid-58475678_1/courses/EECT101-50C-C1-201430/EECT101-50C-C1-201430_ImportedContent_20150114121945/ee101_vids_capacitors.htm

## Slide 24
Measure the following: |  |  |  |  | Expected: |  | Measured: | 
a. | 4 capacitors, incl 1 that is electrolytic |  |  |  | 4.7 | pF | 4.95 | pF
 |  |  |  |  | 0.0033 | µF | 0.00329 | µF
 |  |  |  |  | 0.01 | µF | 0.0096 | µF
 |  |  |  |  | 4.7 | µF | 3.329 | µF
Lab 5 - Test Equipment, Capacitors, and Inductors
Capacitors

## Slide 25
Measure the following: |  |  |  |  | Expected: |  | Measured: | 
a. | 3 inductors |  |  |  | 100 | µH | 107.76 | µH
 |  |  |  |  | 22 | mH | 20.64 | mH
 |  |  |  |  | 100 | mH | 97.3 | mH
Lab 5 - Test Equipment, Capacitors, and Inductors
Hand-wound Inductors
Looked up the inductance value for the rings

## Slide 26: Lab 6 – Learn to Solder
Objective
  Learn how to Solder and unsolder
Equipment and Material
  Soldering Iron.
  Wet Sponge
  Angle Cutter
  Pliers
  Wires
  Small proto board
Research and Information
  Watched videos on how to solder:
    Soldering Techniques: Part 6, from Ivy Tech Engineering
    How to solder & unsolder review from YouTube
    Beginner, How to solder from YouTube
    Soldering Techniques from YouTube

## Slide 27: Lab 6 – Learn to Solder
Solder on to a proto board:
4 Resistors of 2 different sizes
1 Electrolytic Capacitor
1 Signal diode
3 Rectifier Diodes of 2 different sizes
1 Inductor
1 Transistor

## Slide 28: Lab 6 – Learn to Solder

## Slide 29
Lab 7-A – CD-1 Checkout
Objective
  Identify all the different components in an old CMOS/TTL CD-1 board from the 80’s
  Identify the two families of ICs
Equipment and Material
  Eli – CMOS/TTL Designer, CD-1, Series# 40512
Research and Information
  Review components from previous labs.

## Slide 30
Lab 7-A – CD-1 Checkout

## Slide 31
Lab 7-A – CD-1 Checkout
Resistors:
  9 - 1000Ω
  4 - 150 Ω
  1 - 75 Ω
  1 - 2 Ω
  1 – 4.7k Ω
  4 – 470k Ω
  1 - 47 Ω
Potentiometer
  100k
Capacitor
Diodes (+)
Rectifier

## Slide 32
Lab 7-B – First Solder Kit
Objective
  Solder together a Flashing LED Vellman Kit
Equipment and Material
  Soldering Iron.
  Wet Sponge
  Angle Cutter
  Vellman Kit (MK102) with schematic
    Resistors: 2 @ 1kΩ, 2 @ 10KΩ
    Trimmers: 2 @ 250K
    Transistors: 2 – BC547
    Electrolytic Capacitors: 2 @ 10µF
    LEDs: 2 – 5mm
Research and Information
  Review components from previous labs.

## Slide 33
Lab 7-B – First Solder Kit

## Slide 34
Lab 7-B – First Solder Kit

## Slide 35
Lab 8 – 555 Timer Chip
Objective
  Find formula to set frequency and calculate values needed for frequencies: 0.5Hz, 1Hz, and 2Hz
  Verify frequencies with an oscilloscope
  Learn about common cathode and common anode LEDs and why current limiting resistors are needed
Equipment and Material
Research and Information
  555 Timer Chip and formula at http://www.doctronics.co.uk/555.htm
  DMM
  Oscilloscope
  Power Supply
  LCR Meter
  555 Timer Chip
  Solderless breadboard
  Resistors
  Capacitors
  LED
  Jumper wires

## Slide 36
Lab 8 – 555 Timer Chip

## Slide 37
Lab 8 – 555 Timer Chip
Measured Rb
Calculated Rb for each frequency
F = 1.44/((RA + 2RB)*C) |  |  | Duty Cycle = 1 - (RB/(RA + 2RB)) |  | 
F | 0.5 |  | 50.97% |  | 
C | 1.00E-05 |  |  |  | 
RA | 5.60E+03 |  |  |  | 
RB | 1.41E+05 |  |  |  | 
F = 1.44/((RA + 2RB)*C) |  |  | Duty Cycle = 1 - (RB/(RA + 2RB)) |  | 
F | 1 |  | 51.94% |  | 
C | 1.00E-05 |  |  |  | 
RA | 5.60E+03 |  |  |  | 
RB | 6.92E+04 |  |  |  | 
F = 1.44/((RA + 2RB)*C) |  |  | Duty Cycle = 1 - (RB/(RA + 2RB)) |  | 
F | 2 |  | 53.89% |  | 
C | 1.00E-05 |  |  |  | 
RA | 5.60E+03 |  |  |  | 
RB | 3.32E+04 |  |  |  | 
Ra = | 5.6 KΩ | Rb = | 139 kΩ | C = | 10 µF | F = | 0.49 Hz
Ra = | 5.6 KΩ | Rb = | 69 kΩ | C = | 10 µF | F = | 1 Hz
Ra = | 5.6 KΩ | Rb = | 33 kΩ | C = | 10 µF | F = | 2 Hz

## Slide 38
Lab 8 – 555 Timer Chip

## Slide 39
Lab 9 – Filters
Objective
  Build an RC lowpass Filter
  Measure the frequency response from 10Hz to 100,000Hz.
  Find cutoff frequency fc
Equipment and Material
  LCR Meter
  Oscilloscope
  Function Generator
Research and Information
  Low Pass Filter are made:
    Low frequency (up to 100kHz) = RC (Resistor-Capacitor) network
    High frequency (above 100kHz) = RLC (Resistor-Inductor-Capacitor) network
  Formulas

## Slide 40
Lab 9 – Filters
Formulas Used

## Slide 41
Resistor | Units | Capacitor | Units | Frequency | Vin | Units | Vout | Units | Capacitive reactance Xc= 1/(2πfC) | Units
985 | Ω | 0.478 | µF | 10 | 1 | V | 820 | mV | 7.50841E-06 | Ω
 |  |  |  | 20 | 1 | V | 940 | mV | 1.50168E-05 | 
 |  |  |  | 30 | 1 | V | 970 | mV | 2.25252E-05 | 
 |  |  |  | 40 | 1 | V | 980 | mV | 3.00336E-05 | 
 |  |  |  | 50 | 1 | V | 980 | mV | 3.7542E-05 | 
 |  |  |  | 60 | 1 | V | 980 | mV | 4.50504E-05 | 
 |  |  |  | 70 | 1 | V | 980 | mV | 5.25588E-05 | 
 |  |  |  | 80 | 1 | V | 980 | mV | 6.00673E-05 | 
 |  |  |  | 90 | 1 | V | 960 | mV | 6.75757E-05 | 
 |  |  |  | 100 | 1 | V | 950 | mV | 7.50841E-05 | 
 |  |  |  | 200 | 1 | V | 880 | mV | 0.000150168 | 
 |  |  |  | 300 | 1 | V | 760 | mV | 0.000225252 | 
 |  |  |  | 400 | 1 | V | 660 | mV | 0.000300336 | 
 |  |  |  | 500 | 1 | V | 580 | mV | 0.00037542 | 
 |  |  |  | 600 | 1 | V | 520 | mV | 0.000450504 | 
 |  |  |  | 700 | 1 | V | 450 | mV | 0.000525588 | 
 |  |  |  | 800 | 1 | V | 410 | mV | 0.000600673 | 
 |  |  |  | 900 | 1 | V | 380 | mV | 0.000675757 | 
 |  |  |  | 1,000 | 1 | V | 312 | mV | 0.000750841 | 
 |  |  |  | 2,000 | 1 | V | 164 | mV | 0.001501681 | 
 |  |  |  | 3,000 | 1 | V | 112 | mV | 0.002252522 | 
 |  |  |  | 4,000 | 1 | V | 86 | mV | 0.003003363 | 
 |  |  |  | 5,000 | 1 | V | 66.4 | mV | 0.003754203 | 
 |  |  |  | 6,000 | 1 | V | 56 | mV | 0.004505044 | 
 |  |  |  | 7,000 | 1 | V | 48 | mV | 0.005255885 | 
 |  |  |  | 8,000 | 1 | V | 40.4 | mV | 0.006006725 | 
 |  |  |  | 9,000 | 1 | V | 36 | mV | 0.006757566 | 
 |  |  |  | 10,000 | 1 | V | 32 | mV | 0.007508406 | 
 |  |  |  | 20,000 | 1 | V | 16.8 | mV | 0.015016813 | 
 |  |  |  | 30,000 | 1 | V | 11.8 | mV | 0.022525219 | 
 |  |  |  | 40,000 | 1 | V | 9.7 | mV | 0.030033626 | 
 |  |  |  | 50,000 | 1 | V | 7.8 | mV | 0.037542032 | 
 |  |  |  | 60,000 | 1 | V | 7 | mV | 0.045050439 | 
 |  |  |  | 70,000 | 1 | V | 6 | mV | 0.052558845 | 
 |  |  |  | 80,000 | 1 | V | 5.5 | mV | 0.060067252 | 
 |  |  |  | 90,000 | 1 | V | 5 | mV | 0.067575658 | 
 |  |  |  | 100,000 | 1 | V | 4.8 | mV | 0.075084064 | 
Lab 9 – Filters
Chart: V-out at Different Frequencies
| 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 20000 | 30000 | 40000 | 50000 | 60000 | 70000 | 80000 | 90000 | 100000
 | 820 | 940 | 970 | 980 | 980 | 980 | 980 | 980 | 960 | 950 | 880 | 760 | 660 | 580 | 520 | 450 | 410 | 380 | 312 | 164 | 112 | 86 | 66.4 | 56 | 48 | 40.4 | 36 | 32 | 16.8 | 11.8 | 9.7 | 7.8 | 7 | 6 | 5.5 | 5 | 4.8
Cut-off Frequency Fc = 1/(2πRC) | 
338.0305909 | Hz

## Slide 42
Lab 9 – Filters

## Slide 43
Lab 10 – Square Wave to
Sine Wave
Objective
  Convert a square wave into a sine wave
Equipment and Material
  Multisim
  Function Generator
  Oscilloscope
  4 - 22µF Capacitors
  4 - 100Ω Resistors
Research and Information
  Watched Youtube Video: “Change a square wave into a sine wave (3 pole RC Filter)”

## Slide 44
Lab 10 – Square Wave to
Sine Wave
Multisim

## Slide 45
Lab 10 – Square Wave to
Sine Wave

## Slide 46
Lab 11A – Troubleshoot/Fix
Home Electronic
Objective
  Troubleshoot/fix a desktop
Equipment and Material
  Desktop Computer:
    HP Pavilion: a6403w
Research and Information
  Upgrades for desktop computer

## Slide 47
Lab 11A – Troubleshoot/Fix
Home Electronic
Network Connection not working:
  Tested network integrated port by connecting an Ethernet cable and found that it was not working.
  Took out Modem and replaced it with an Ethernet card.
USB port not working:
  Connected a standard USB mouse to all the port (4 in the back and 2 in the front) all worked.
Original Problem from Home

## Slide 48
Lab 11A – Troubleshoot/Fix
Home Electronic
Tested the optical drive by putting in a CD, it was working.
Noticed a lot of dust inside. Recommend to clean out.
CMOS battery is dead, needs replaced. (CR2032, 3V, lithium battery)
RAM is 2 – 1G, recommend upgrade to 2 – 2G.
No rear case fan, recommend installing a 80mm fan.
Defragged through Command Propt
Recommend upgrading CPU to an Intel Pentium Processor E2220
Other thing found

## Slide 49
Lab 11A – Troubleshoot/Fix
Home Electronic

## Slide 50
Lab 11B – Test
7400Series Chips
Objective
  Build a tester with LED to test 7400 Series Chips
Equipment and Material
  DC Power Supply
  DMM
  Solderless Breadboard
  SN7432 Chips
  1k Resistor
  4 LEDs
Research and Information
  Schematic for 7400 Series Chips

## Slide 51
Lab 11B – Test
7400Series Chips
SN7432 – 2 input OR gate

## Slide 52
Lab 11B – Test
7400Series Chips

## Slide 53
Lab 12 – Lissajous Pattern
Objective
  Display a circle or an ellipse on an oscilloscope
Equipment and Material
  Oscilloscope (x/y Mode)
    Ch. 1 – Horizontal
    Ch. 2 – Vertical
  2 Function Generators
Research and Information
  Watched: #48: Basics of lissajous Patterns on an Oscilloscope.”

## Slide 54
Lab 12 – Lissajous Pattern

## Slide 55
Lab 13 – AC to DC
Power Supplies
Objective
  Convert AC to DC
Equipment and Material
  Oscilloscope
  Function Generators
  Solderless Breadboard
  4- Diodes (1N4148)
  1- Capacitor (100µF)
Research and Information
  Watched video: “AC to DC Converter: Bon Jespersen”

## Slide 56
Lab 13 – AC to DC
Power Supplies
Make an schematic on Multisim

## Slide 57
Lab 13 – AC to DC
Power Supplies
Built a converter on a breadboard

## Slide 58
Lab 14 – ESD
Objective
  Know what ESD is and how it can affect electronic devices
  Know how to prevent or minimize ESD
  Find the approximate voltage generated by:
    Masking Tape
    Scotch Tape
    Wool Sweater
    Walking across the carpet in the winter
Research and Information
  Definition of ESD on: http://whatis.techtarget.com/definition/electrostatic-discharge-ESD
  Found how to prevent ESD on website: http://www.minicircuits.com/app/AN40-005.pdf

## Slide 59
Lab 14 – ESD
ESD (Electro Static Discharge)
  Is the release of static electricity when 2 things come in contact with each other.
  Some examples are:
    Dragging your feet across a carpet and touching a metal object or a person.
    Static electricity from dried clothes in dryer.
    Lightening bolt
ESD Info
  While most of the ESD are harmless to the human body. It is very damaging to electronic devices.
  Two kids of damages can occur:
    Catastrophic Damage: The device stops working immediately.
    Latent Damage: Device appears to continue working, but could stop in the future.

## Slide 60
Lab 14 – ESD
ESD Prevention
  In the work Area one can use Anti Static:
    Table mat
    Floor mat
    Tweezers
    Carrier tape
    Bag
  Personnel can
    Discharge themselves by wearing a ground antistatic wrist-strap
    Use antistatic:
      Smock
      Finger cots

## Slide 61
Lab 14 – ESD

## Slide 62
Lab 15 – Test Old
0-30VDC
Objective
  Test voltage with multimeter:
    5V
    10V
    20V
    30V
Equipment
  DMM
  0-30 VDC
Research and Information
  Review how to test voltage from previous labs

## Slide 63
Lab 15 – Test Old
0-30VDC

## Slide 64
Lab 16 – Final Project
Objective
  Solder together a Flashing European Siren (AK-100)
Equipment and Material
  DMM
  Function Generator
  Soldering Iron.
  Wet Sponge
  Angle Cutter
  AmeriKit (AK-100) with schematic
    9 Resistors: 1 @ 68Ω, 2 @ 470Ω, 1 @ 1kΩ, 2 @ 10kΩ, 2 @ 22kΩ, 1 @ 47kΩ, 1 VR @ 200Ω Trim Pot
    Capacitors: 2 @ .02µF, 3 @ 10µF, 1 @ 100µF
    Semiconductors: 2 – 2N3904, 1 – IC 555, 2 LED (red)
    Breadboard
    Speaker
    Wire 22AWG solid 3’
Research and Information
  Read instruction in the kit

## Slide 65
Lab 16 – Final Project
Test all components
Solder components in this order
  Resistors
  Capacitors
  Semiconductors
  Speaker
  Battery snap
Check soldering
Connect battery to see if it works

## Slide 66
Lab 16 – Final Project
Soldering

## Slide 67
Lab 16 – Final Project
It works!!!