## Slide 1: Lab Notebook for EECT 121
By: Seth wills
Lab Partner Were Jarred Clark, Donald Stanley and Alex Drummond Beside the +/- 9 Volt Power Supply

## Slide 2: Lab 1: The Switching Diode Date: 09/05/18
The purpose of this Lab was to demonstrate how a switching diode functions and build and test the diode in a circuit while using multisim and using the equipment in the lab.
Equipment Needed:
Gwinsek GDM-8245 Multimeter
820 Ohm Resistor
1N4128 Se Switching Diode
1N4001 Switching Diode

## Slide 3: Lab 1: Part 2
This multisim is a simulation of the 1N4148 diode in the forward and reverse bias. The diodes we used have a voltage drop of .7 volts. In the forward bias phase you get an output of a high (shown as 8.328 Volts)but in the reverse bias you get a low(shown as 7.462 NanoVolts) output.
Forward bias
Reverse bias

## Slide 4: Lab 1:Part 3
This multisim is a simulation of the 1N4001 diode in the forward and reverse bias. The diodes we used have a voltage drop of .7 volts. In the forward bias phase you get an output of a high (shown as 8.353 Volts)but in the reverse bias you get a low(shown as 10.051 MicroVolts) output.
Forward bias
Reverse bias

## Slide 5: Lab 1: Part 4
Applied voltage
Forward bias
Part: 1N4148

## Slide 6: Lab 1
Output voltage in forward bias
Output voltage in forward bias #2
Output voltage in reverse bias

## Slide 7: Lab 1: Part 7
PUT PICTURES HERE
Data sheet for the diode, displaying which side the cathode (black band)

## Slide 8: Lab 1: Observation
A diode is composed of two biases one is forward and the other is reverse. When one is in forward bias it is considered on. When the diode is in reverse bias it is consider to be off.

## Slide 9: Lab 2:LEDs Date: 09/05/18
The purpose of this lab is to demostrate how a LED functions and build and test the LEDS while using multisim and using the equipment in the lab.
Parts and Equipment Needed:
560 ohm Resistor
330 ohm Resistor
680 ohm Resistor
LED – 08L53GD - Green
LED – 08L53YD - Yellow
LED – 08L53ED – Amber (RED)
HY1802D DC Power Supply Gwinstek GDM-8245 Multimeter
Breadboard

## Slide 10: Lab 2: Part 2
This is the simulation of the three LEDs that we tested. The color were red, green, and yellow. We used 3 different resistors for each LED. For the red led we used 560 ohms, for the yellow led we used the 680 ohm resistors and for the green led we used the 330 ohm resistor.

## Slide 11: Lab 2: Part 3
circuit set up
Voltage before going to the LED

## Slide 12: Lab 2: Part 4
Input voltage
Voltage before after resistor
& measurement before LED

## Slide 13: Lab 2 Part 5
Voltage when the LED turns off
Green LED

## Slide 14: Lab 2: Observations
For each color of led we had to use a different resistors because each led has different voltage dissipation characteristics to have the light visible.

## Slide 15: LAB 3: Zener Diode
The purpose of this lab is to demonstrate how a Zener Diode functions and build and test the Zener Diodes while using multisim and using the equipment in the lab.
Parts needed:
1k Ohm Resistor
ZENER 1N4728A
ZENER, 1N4732A
ZENER, 1N4733A
ZENER 1N4735A
ZENER, 1N4736A
Equipment Needed:
1 – GDM-8245 Multi-meter
1 – HY1802D DC Power source
1 – Breadboard

## Slide 16: Lab 3: Part 2
This is the simulation and simulation results of 5 different zener diodes

## Slide 17: Lab 3: Part 3
ADD Pictures

## Slide 18: Lab 3: Part 4

## Slide 19: Lab 3: Observations
Demonstrated in this lab we observed that zener diodes work differently than regular diodes in the previous labs. Zener diodes works as a voltage regulator.

## Slide 20: Lab 4: 9V +/- Power Supply Lab Partner was Jarred Clark
The Purpose of this Lab is to Build and design/test a +/- 9 Volts DC Power Supply
Equipment Needed:
HY1802D DC Power Supply Gwinstek GDM-8245 Multimeter
Circuit Board
Soldering Gun and Solder
12.6 volt Transformer
Fuse Holder/fuse
Switch
4-1N4007
4-400uf Capacitors
2- Orange LED’s
2-20 ohm Resistors
LM 317 and LM 337
2-330 Ohm Resistors
2- Potentiometers
2-240 Ohm Resistors
2-100uf Capacitors
2-90 Ohm resistors for the load
2-10 Ohm Resistors for the load

## Slide 21: Lab 4: Part 2
This is the multisim built from scratch in order to create and build/Test the +/- 9 Volts DC Power Supply

## Slide 22: Lab 4: Part 3
This is our BOM (Bill of Materials) that we made in order to total up the cost and order all the parts for the Power Supply. Minimum cost was 25 dollars and we totaled up to $16.02

## Slide 23: Lab 4: Part 4
Datasheet for LM337
Datasheet for LM317

## Slide 24: Lab 4: Part 5
This is the dc power supply with only the positive led working, but we found out in the negative side that we had a cold solder joint in the ground bus which caused the LED to become inactive
Our startup time for our power supply was 75 milliseconds

## Slide 25: Lab 4: Part 6
Measuring the 91 ohm resistor which is the load
This is the complete build for the power supply after we fixed the cold solder joints in the ground bus

## Slide 26: Lab 4: Part 7
This is the negative voltage coming from thee put of the power supply
This is the positive voltage coming from thee put of the power supply

## Slide 27: Lab 4: Part 8
This is the solder job done by Jarred Clark and Seth Wills.
The transformer that we received from electronix express was manufactured wrong where the blue wire is not the center tap but was one of the inputs to the rectifier

## Slide 28: Lab 4: Part 8
This is the positive voltage after we applied the 91 ohm load
This is a picture of Seth and I soldering the components onto the board

## Slide 29: Lab 4: Part 9
The load resistance is measured from the multimeter of 90.28 ohms

## Slide 30: Lab 4: Observations
When building the +/- 9 volts DC Power Supply we ran into multiple issues such as the transformer being manufactured wrong. The potentiometer were not adjusting the voltage for the output due to a cold solder joint in the ground bus. Their for at the beginning our negative LED was unable to function. The 20 Ohm resistor in our pi filter was causing to much of a voltage drop and only giving us 7 volts for the output so we replaced the resistor with a wire jumper and then the output turned to 9 volts and the potentiometer started to function right. This was mainly due to an oversight in the calculations in the actual output of the step down transformer.

## Slide 31: Lab 5: Common Emitter Amplifier
The purpose of this lab is to demostrate how a transistor is used in a common emitter amplifier configuration.
Equipment Need:
1 – GDM-8245 Multi-meter
1 – HY1802D DC Power source
1 – Breadboard
1- LED
1-2N2222A Transistor
1- 220 ohm resistor
1- 500 resistors

## Slide 32: Lab 5: Common Emitter Amplifier
Insert Multisim for Lab 5

## Slide 33: Lab 5 Part: 3
Vin= | 5 | 
Q1= | 2N2222A | 
RB= | 220 | 
RC= | 500 | 
LED= | 08LX330 RED | 
LED Min Current= | 1 | A
LED VF= | 2.682 | V
VCE when LED is "on"= | 2.025 | V
VCE when LED is "off"= | 3.974 | V
This is the spreadsheet for the calculated results for Lab 5

## Slide 34: Lab 5: Part 3
This is a video of the transistor being used as a common emitter amplifier. We used a red led, 1 390 ohm resistor and 2 1k resistors in parallel

## Slide 35: Lab 5: Part 4
This is the Oscilloscope reading for Channel 1
This is the complete build of Lab 5’s Circuit

## Slide 36: Lab 5: Observations
We observed that one way to use the diode as a switch is by changing the collector voltage, in our case it was at 3V where it turned off.

## Slide 37: Lab 6: Common Emitter (CE) Amplifier
Equipment Need:
1 – GDM-8245 Multi-meter
1 – HY1802D DC Power source
1 – Breadboard
1-2N2222A Transistor
5- 1k, 220k, 50, 22k, 50 ohm resistors
3-1uf, 47uf and 47uf capacitor

## Slide 38: Lab 6: Part 2

## Slide 39: Lab 6: Part 3
R1 | 2.20E+04 |  |  | 
RC | 2.20E+05 |  |  | 
R2 | 5.00E+01 |  |  | 
RE | 5.00E+01 |  |  | 
RL | 1.00E+03 |  |  | 
VIN | 1.00E-03 |  |  | 
VCC | 9 |  |  | 
VOUT | 1.00E-01 |  |  | 
C1 | 04.7E-06 |  |  | 
C2 | 04.7E-06 |  |  | 
CE | 01.0E-06 |  |  | 
Q1 | 2N2222A |  |  | 
FREQ | 1.00E+03 |  |  | 
IE |  |  |  | 
VC | 9 |  |  | 
This is the Excel Sheet for the Calculation results for Lab 6

## Slide 40: Lab 6: Part 4
This is the Oscilloscope reading for channel1 for lab 6
This is the complete build for the circuit for lab 6

## Slide 41: Lab 6: Observations
We had a few issues calculating the resistor values and capacitor values, and it was a little difficult to build. We compared our results to an another example lab notebook. Our end result produced a cleaner reading than they received on example oscilloscope.

## Slide 42: Lab 7: Using a JFET to flash an LED
The Purpose of this is lab is to design, build/test a JFET circuit and using it to flash an LED.
Equipment Needed:
1-2N5457 JFET Amplifier
2- 470 Ohm Resistors
1- Yellow LED
1- Gwinstek Function Generator
1 – GDM-8245 Multi-meter
1 – HY1802D DC Power source

## Slide 43: Lab 7: Part 2
We had to manually design the JFET in Multisim

## Slide 44: Lab 7: Part 3
The datasheet for the JFET
2N5457
This the multimeter for the 470 ohm resistor which is reading 470.43 Ohms

## Slide 45: Lab 7: Part 4
Preview attachment 20181205_175347_001.mp4
20181205_175347_001.mp4
365 KB
This is the video showing the function generator and the Led flashing on and off
This is the Oscilloscope reading for the led turning on and off

## Slide 46: Lab 7: Part 5
This is the picture of the complete build for Lab 7

## Slide 47: Lab 7: Observations
The circuit was not too difficult to build. The only complication that we ran into is that we put the JFET in backwards. We changed the frequency to make it flash slower and faster.

## Slide 48: Lab 8: Using the JFET as a Amplifier My Lab Partner was Jarred clark
The Purpose of this lab is to test and build an Amplifier circuit using a JFET
Equipment Needed:
1-2N5457 JFET Amplifier
1- Gwinstek Function Generator
1 – GDM-8245 Multi-meter
1 – DC Power Supply
2- 1uf Capacitors
1-33uf capacitor
1-68k ohm resistor
1- 22k ohm resistor
1-100k resistor as a load
1- 3.3k ohm resistor

## Slide 49: Lab 8: part 2

## Slide 50: Lab 8: Part 3
Measuring the 22k ohm resistor with the multimeter

## Slide 51: Lab 8: Part 4
Measuring the 33k Ohm resistor using the multimeter
This is the frequency that was the input for the circuit which is a 1kHz

## Slide 52: Lab 8: Part 5
This is the false circuit that was built that did not function correctly
The amplitude from the function generator was set to high which was causing the channel two to clip off

## Slide 53: Lab 8: Part 6
This is the correct circuit that is build that gave us the correct results
This is the correct reading for the oscilloscope which the two sine waves are almost 180 out of phase of eachother

## Slide 54: Lab 8: Part 7
This is the picture of the Lab DC Power Supply which we used for the -5 volt and the 9 volt inputs

## Slide 55: Lab 8: Part 8
This is the correct multisim for lab 8 that is fully functional

## Slide 56: Lab 8: Part 9
These are the finalized pictures of the oscope and circuit that is fully functional

## Slide 57: Lab 8: Observations
Used the power supply to produce -5 volts by switching the leads. Problems found with current limiter on the power supply was set to low. We had the JFET in the circuit backwards. We had to try the hook up multiple times, because we were getting no reading on the oscilloscope. And we were having trouble connecting the amount of alligator clips together because it was too many for a small circuit. We redid the circuit with a load and a few different resistor values and then it started to work correctly

## Slide 58: Lab 9: High pass filter
The Purpose of this Lab was to build and calculated a high pass filter using multi-sim and excel, Which is used to filter frequencies above a set range

## Slide 59: Lab 9: Part 2
This is the multisim simulation for Lab 9

## Slide 60: Lab 9: pArt 3
HIGH PASS FILTER |  | 
A0= | 1 | 
a1= | 1.4142 | 
b1= | 1 | 
C= | 100.0E-9 | 
C1= | 100.0E-9 | 
C2= | 100.0E-9 | 
R1= | 2.3E+3 | 
R2= | 1.1E+3 | 
fc= | 1.0E+3 | Hz
This is the excel spreadsheet for Lab 9

## Slide 61: Lab 10: Low pass filter
The purpose of this lab was to build and calculated a high pass filter using multi-sim and excel, Which is used to filter frequencies with a mid range

## Slide 62: Lab 10: Part 2
This is the multisim simulation for Lab 10

## Slide 63: Lab 10: Part 3
LOW PASS FILTER |  |  | 
A0= | 1 |  | 
a1= | 1.4142 |  | 
b1= | 1 |  | 
C1= | 22.00E-9 | 4.7E-08 | 
C2= | 44.00E-9 |  | 
R1= | 3.82E+3 |  | 
R2= | 6.41E+3 |  | 
fc= | 1000 | Hz | 
This is the excel spreadsheet for Lab 10

## Slide 64: Lab 11: Band-Pass Filter
The Purpose of this Lab was to build and calculated a high pass filter using multisim and excel, Which is used to filter frequencies with a mid range and is considered a Mid-pass filter

## Slide 65: Lab 11: Part 2
This is the multisim simulation for Lab 11

## Slide 66: Lab 11: Part 3
R1 | 7.96E+03 | 
R2 | 31.83E+3 | 
R3 | 80.38 | 
C | 100.0E-9 | 
C1 | 100.0E-9 | 
C2 | 100.0E-9 | 
AM | -2.0 | 
Q | 10.0 | 
fm | 1000 | Hz
B | 157.08 | bandwidth
Q | 10.00E+0 | filter quality
Am | 2.00E+0 | gain at fm
This is the excel spreadsheet for Lab 11

## Slide 67: Lab 12: Notch Filter
The Purpose of this Lab was to build and calculated a high pass filter using multisim and excel, The Notch filter is used to isolate specific frequencies in a circuit and filter them out.

## Slide 68: Lab 12: Part 2
This is the multisim simulation for Lab 12

## Slide 69: Lab 12: Part 3
fm= | 1000 |  | Mid Freq
G= | 5.7 |  | Inner Gain
A0= | 6 |  | Passband Gain
Q= | -135.14E-3 |  | Rejection Gain
C= | 100.00E-9 |  | 
C1= | 100.00E-9 |  | 
C2= | 100.00E-9 |  | 
C3= | 200.00E-9 |  | 
R= | 1.59E+3 |  | 
R1= | 1000 |  | 
R2= | 4700 |  | 
R3= | 1.59E+3 |  | 
R4= | 1.59E+3 |  | 
R5= | 795.77E+0 |  | 
This is the excel spreadsheet for Lab 12